## Slide 1: LAB- 5 Study the concept of VLAN
Dolly.bharvada@darshan.ac.in
Computer Science & Engineering Department
Prof. Dolly A. Bharvada
Computer Network(CN)
DU #2104CS301

## Slide 2
✓
Outline
  What is VLAN?
  Need of VLAN
  Advantages of VLANs
  Access and trunk interface
  Configuration of VLAN
  Step to configure VLANs

## Slide 3: Broadcast in LANs
Here 2 different networks LANs switch forwards traffic.
A broadcast domain is a set of devices that can receive broadcast messages from each other.
Broadcast messages are packets that are sent to all devices on the same network, such as ARP requests or DHCP offers.
Broadcast messages are useful for discovering and configuring network devices, but they can also consume bandwidth and cause network congestion if there are too many devices or too much traffic on the same network.

## Slide 4: Broadcast in LANs
Two different LANs
LAN 1
LAN 2

## Slide 5: Broadcast in LANs
Design a two LANs which has one switch and three PCs. LAN 1 PCs can’t communicate with LAN 2
If you connect the system as shown in figure then LAN 1 PC can communicate with other
So how to separate them logically.
What is solution?
LAN1
Solution of this is VLAN
LAN 2

## Slide 6
VLANs are logical grouping of devices
in the same broadcast domain.
logical grouping
same broadcast domain
VLAN – Virtual LAN

## Slide 7: VLANs
192.168.10.2
192.168.10.3
192.168.10.4
192.168.10.6
192.168.10.5
192.168.10.7
VLAN 1
VLAN 3
VLAN 2

## Slide 8: VLAN
Virtual LANs or VLANs are usually configured on switches by placing some devices into one broadcast domain and some devices into some other broadcast domain.
VLANs keep traffic from different networks separated when traversing shared links and devices within a topology.
Each VLANs acts as a subgroup of the switch ports in an Ethernet LAN.
VLAN 2

## Slide 9: VLAN Example
VLANs per port view

## Slide 10: Advantages of VLAN
It improves the security by reducing the number of end-stations that receive copies of BUM (Broadcast, Unicast, and Multicast) traffic.
It creates smaller fault domains by isolating different groups of devices in separate broadcast domain.
It reduces the CPU overhead on each device in the LAN by limiting the number of broadcast frames received.
It improves network performance and speed of failure recovering.

## Slide 11: Access and Trunk Interfaces
Ethernet interfaces can be configured in two ways:
  Access ports
  Trunk ports.

## Slide 12
An access port can have only one VLAN configured on the interface; it can carry traffic for only one VLAN.

## Slide 13
An access port can have only one VLAN configured on the interface; it can carry traffic for only one VLAN.
Access Port
Access Port
Access Port
Access Port
Access Port
Access Port

## Slide 14: VLANs on multiple switches
VLANs spanned on multiple switches without Trunking

## Slide 15
A trunk port can have two or more VLANs configured on the interface; it can carry traffic for several VLANs simultaneously.

## Slide 16
Trunk Port
Trunk Port
Access Port
Access Port
Access Port
Access Port
Access Port
Access Port
A trunk port can have two or more VLANs configured on the interface; it can carry traffic for several VLANs simultaneously.

## Slide 17: VLAN Tagging
VLAN trunking allows switches to forwards frames from different VLANs over a single link called trunk.
This is done by adding an additional header information called tag to the Ethernet frame.
The process of adding this small header is called VLAN tagging.
VLAN Data Frame
Destination Address
Source
Address
6 bytes
6 bytes
VLAN
Tag
Length/
Type
4 bytes
2 bytes
Data
46 - 1500 bytes
4 bytes
FCS
TPID
PRI
CFI
VID
2 bytes
3 bits
1 bits
12 bits
TPID -
Tag Protocol Identifier, indicating the frame type, i.e., IEEE 802.1Q frame.
PRI -
Priority, value from 0 to 7
CFI -
0 -> MAC encapsulated, 1 -> non-encapsulated
VID -
VLAN ID, ranges value from 1 to 4094

## Slide 18: Configure VLAN
Example of a switch with two VLANs

## Slide 19: Steps to create VLANs
In the CLI tab of the switch type conf t and press enter
Type vlan 10 on the prompt and press enter
Type name A BLOCK on the prompt and press enter
Enter exit on the prompt and press enter
Type vlan 20 on the prompt and press enter
Type name C BLOCK on the prompt and press enter
Enter end on the prompt and press enter
Type show vlan brief and press enter
Type conf t and press enter
Type interface range fa0/1 – 4
Type switchport access vlan 10
Type switchport mode access
Type exit

## Slide 20: Steps to create VLANs
Type exit and press enter
Type interface range fa0/15-18
Type switchport access vlan 20
Type switchport mode access
Type end and press enter
Type show vlan brief and press enter

## Slide 21: Sample VLANs
1)
2)
3)

## Slide 22: Thank you